## Slide 1
SmartGrid AI Audit Framework
Cyber-Physical Monitoring and Audit Intelligence for Modern Smart Grid Systems
Aditya Sanjay Jadhav (242050010)
Guide: Shrinivas Khedkar | Dept. of Computer Engineering & IT, VJTI Mumbai

## Slide 2
Problem Statement: Insufficient Cyber-Physical Anomaly Detection in Smart Grids
Traditional Monitoring
Dual Vulnerabilities
Lack of Explainability
Resource Allocation Gap
Need for Real-Time Integration
Traditional monitoring relies on static thresholds and periodic audits
Cyber-physical systems expose electrical and communication vulnerabilities simultaneously
Existing approaches lack operational decision support and explainability
Gap between anomaly detection and audit resource allocation
Need for real-time SCADA-integrated monitoring with audit intelligence

## Slide 3
Motivation: Dynamic Audit Intelligence for Distributed Grid Environments
Static auditing limits
Actionable operator guidance
Prioritization for critical risks
Real-time integration
Explainability for trust
Static auditing increases cost or leaves vulnerabilities undetected
Operators require actionable guidance beyond classification accuracy
Audit prioritization needed to address critical risks efficiently
Real-time supervisory integration essential for operational deployment
Explainability critical for operator trust and decision transparency

## Slide 4
Research Objectives: Building an Explainable SCADA-Integrated Audit Framework
1
2
3
4
5
1. Design cyber-physical anomaly detection across electrical and communication features
2. Implement explainable deviation-based scoring for transparent decisions
3. Develop audit decision framework prioritizing high-risk assets under constraints
4. Integrate Rapid SCADA as live telemetry source for real-time monitoring
5. Separate experiment evaluation from live operational monitoring for clarity

## Slide 5
Research Gap: From Conceptual Models to Operational Deployment
1
Detection vs. Audit
2
SCADA Integration
3
Operator Visualization
4
Experimental vs Operational
5
Deployment Engineering
Most works focus on detection accuracy without audit allocation
Limited live SCADA integration in existing frameworks
Insufficient operator-facing visualization and explainability
Lack of separation between experimental and operational modes
Need for deployment-oriented engineering with honest telemetry provenance

## Slide 6
Base Paper: AI-Driven Audit Framework for Distributed Smart Grids
Priyadarsini (2025)
Multi-Agent Grid
Reported Metrics
Conceptual Foundation
Simulation Focus
The paper by Priyadarsini (2025) establishes a clear linkage between anomaly detection outputs and subsequent audit optimization, proposing algorithms that translate detections into prioritized audit tasks.
Describes a multi-agent smart grid architecture that supports dynamic adjustment of audit resources, enabling agents to reallocate inspections in response to evolving anomaly likelihoods and constraints.
Key reported performance metrics include Cost at 42.5%, Coverage at 93.8%, Accuracy at 98.4%, and Risk Mitigation at 87.9%, demonstrating strong simulated effectiveness across objectives.
Presents a strong conceptual foundation that systematically connects anomaly detection signals with audit planning decisions, offering theoretical justification and formal mappings between components.
The work is primarily simulation-oriented and does not include deployment with live SCADA systems, emphasizing modeling and synthetic experiments rather than field implementation.

## Slide 7
Base Paper Limitations: Implementation and Integration Gaps
Limitation 1
Limitation 2
Limitation 3
Limitation 4
Limitation 5
Absence of live SCADA integration and real-time telemetry handling, preventing continuous operational data ingestion and immediate responsiveness.
Limited deployment-oriented system architecture and engineering detail, lacking concrete guidance for production-grade implementation and scaling.
No explicit separation between experiment evaluation and operational monitoring, which risks mixing offline validation with live decision workflows.
Insufficient operator-facing visualization and workflow support, reducing situational awareness and hindering effective human-in-the-loop operations.
Limited emphasis on explainability in live decision pathways, making it difficult to trace, justify, and audit automated operational actions.

## Slide 8
Capability Comparison: Base Paper vs Proposed Framework

## Slide 9
Development Progress of the SmartGrid AI Audit Framework

## Slide 10
Proposed System Overview: Explainable Cyber-Physical Audit Platform
Unified Framework
Two Operational Workspaces
Deviation-Based Scoring
Live Telemetry Pipeline
Operator-Facing Dashboard
Combines anomaly detection, audit intelligence, and SCADA monitoring into a single cohesive platform for end-to-end cyber-physical assurance.
Provides Experiment Running for controlled tests and Rapid SCADA Live for real-time operational monitoring and intervention.
Calculates anomaly scores based on deviations and offers feature-level explainability to pinpoint root causes and contributing signals.
Streams real-time data through Rapid SCADA Web API integration to ensure low-latency ingestion and continuous observability.
Separates experimental views from live operational displays, enabling operators to switch contexts without data overlap.

## Slide 11
System Architecture: Four-Tier Modular Design
Tier 1 — Data Ingestion
Tier 2 — Feature Processing
Tier 3 — Anomaly & Risk
Tier 4 — Operator Interface
Collects raw telemetry from the experiment workspace and Rapid SCADA live streams, ensuring reliable, timestamped ingestion and initial validation for downstream processing.
Processes sensor and operational data to extract features, mapping physical measurements to cyber baselines and normal behavior profiles for context-aware analysis.
Performs anomaly scoring, risk assessment, and audit decision logic using statistical and ML models to prioritize incidents and generate forensic evidence traces.
Provides dashboard visualization, alerts, and explainability tools for operators, enabling interactive investigation, drill-downs, and audit reporting.
The right-side illustration represents the end-to-end SmartGrid AI Audit Framework, showing data flow from SCADA through processing tiers to the operator dashboard.

## Slide 12
Two-Workspace Design: Separation of Experiment and Operational Contexts
1
Experiment Running Workspace
2
Rapid SCADA Live Workspace
3
Isolation of Experimental Outputs
4
Technical Interpretability
Simulation, benchmarking, and ablation analysis conducted across varied grid sizes to evaluate models and configurations in an isolated experimental environment.
Real-time monitoring of operational systems with anomaly scoring and audit support to ensure continuous visibility and rapid response in production.
Prevents experimental outputs from interfering with live operational data by enforcing strict separation and controlled data flows between environments.
Ensures interpretability for both evaluation and monitoring use cases through consistent logging, metrics, and explainability tools across workspaces.

## Slide 13
Rapid SCADA Integration: Live Supervisory Telemetry Pipeline
Rapid SCADA Webstation
PowerShell Bridge
Batched Ingest Design
FastAPI Backend
Calculated Telemetry
Rapid SCADA Webstation at 127.0.0.1:10109 as supervisory telemetry layer
PowerShell bridge retrieves channel data via authenticated Web API access
Batched ingest design to avoid rate-limit instability from per-agent posting
FastAPI backend processes SCADA data through anomaly and audit pipeline
Current telemetry generated via calculated channels within SCADA (not physical field devices)

## Slide 14
100-Agent SCADA Grid: Fixed Asset Topology for Live Monitoring
Generators
Substations
PMUs
Breakers
GEN-01 to GEN-20 — Twenty distributed generation units forming the primary power sources in the topology.
SUB-21 to SUB-50 — Thirty substations handling stepping, routing, and protection across the grid.
PMU-51 to PMU-75 — Twenty-five phasor measurement units providing synchronized measurement points for state estimation.
BRK-76 to BRK-100 — Twenty-five breakers managing sectionalization and fault isolation within the grid.
Implementation note: Implemented as a 300-channel Rapid SCADA model using calculated channels to aggregate and compute derived states for live monitoring and control.

## Slide 15
Algorithm Overview: Deviation-Based Explainable Scoring
Anomaly score
Criticality weight wi
Risk assessment
Threshold-based audit policy
Explainability focus
The anomaly score is defined as Si(t) = wi(dx + dy), where dx denotes the physical deviation and dy denotes the cyber deviation, combining both domains into a single interpretable metric for each asset over time.
wi represents the criticality weight assigned to each asset class; it scales the combined deviation to reflect the operational importance and potential impact of anomalies for different asset types.
Risk is assessed by evaluating the deviation magnitude together with operational importance, enabling prioritization of responses based on both observed deviation severity and asset criticality.
A threshold-based audit policy is applied: if the computed score exceeds a predefined threshold, the system escalates for investigation and response; otherwise routine monitoring is maintained.
The design prioritizes deliberate explainability rather than opaque black-box outputs, ensuring that operators can understand score contributors and maintain operational stability through transparent reasoning.

## Slide 16
Algorithm Flow: Experiment Module vs Rapid SCADA Live Module
Live SCADA Algorithm Flow
Experiment Module Algorithm Flow
Simple Difference
Rapid SCADA generates current values for the 100-agent grid through calculated channels.
The PowerShell bridge reads those live values from the Rapid SCADA Web API.
The backend converts the raw SCADA tags into agent-wise physical and cyber feature vectors.
Each feature is compared against its expected normal baseline and threshold.
Physical deviation and cyber deviation are computed.
A final anomaly score is calculated using the criticality-weighted deviation formula.
The score is compared against the audit threshold.
The system assigns an audit action such as MAINTAIN_AUDIT or INCREASE_AUDIT.
Feature contribution values are computed for explainability.
The dashboard displays live anomaly score, risk score, audit state, and explanation.
The system creates simulated smart-grid agents for the chosen configuration such as N=100, N=200, or N=500.
Synthetic cyber attacks, faults, and scenario variations are injected into the simulation.
Agent-wise physical and cyber states are generated at each simulation step.
The anomaly detection layer evaluates deviations or anomaly probabilities from the simulated inputs.
The hybrid audit scheduler combines anomaly evidence, cost constraints, and policy logic.
Audit actions are allocated dynamically across agents.
The framework compares the dynamic strategy with the fixed baseline audit strategy.
Performance metrics are computed, including attack-rate reduction, cost efficiency, risk mitigation, precision, recall, F1, and accuracy.
Results are written to logs and summary files.
The experiment dashboard displays latest-run analytics, comparisons, and methodology outputs.
The Live SCADA module is a real-time operational pipeline that reads live Rapid SCADA telemetry and turns it into anomaly scores and audit decisions, while the Experiment module is an evaluation pipeline that simulates grid behavior and compares different audit strategies under controlled test scenarios.
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●

## Slide 17
Feature Categories and Baseline Mapping: Cyber-Physical Representation
Physical features
1
Cyber features
2
Type-specific baseline values
3
Criticality weights
4
Normalized deviation scores
5
Voltage, current, frequency, load, power and response time metrics that characterize physical asset behavior under normal and stressed conditions.
Network-related indicators such as latency, packet loss, communication frequency and integrity signals used to assess cyber-layer health.
Expected normal operating conditions defined per asset class to serve as reference baselines for anomaly detection and degradation tracking.
Priority weighting for assets including generator, substation, PMU and breaker to reflect their impact on system stability and response prioritization.
Cross-asset normalized deviation metrics that enable comparison and ranking of anomalies across heterogeneous equipment types.

## Slide 18
Mathematical Formulations and Methodology
Formula Type
Simple Meaning
Used In
Purpose
Physical Deviation (dx)
Normalized distance from expected physical baseline
Both modules
Quantifies how far voltage, current, frequency deviate from normal
Cyber Deviation (dy)
Normalized distance from expected cyber baseline
Both modules
Quantifies latency, packet loss, communication anomalies
Anomaly Score Si(t) = wi(dx + dy)
Weighted sum of physical and cyber deviations
Rapid SCADA Live, Experiment Running
Combines both domains into single interpretable risk metric
Threshold Rule
If Si(t) > threshold then INCREASE AUDIT else MAINTAIN AUDIT
Rapid SCADA Live
Determines audit escalation requirement based on score
Risk Mitigation
Percentage of high-risk events prevented or mitigated
Experiment Running evaluation
Measures effectiveness in reducing operational risk exposure
Cost Efficiency
Ratio of audit resources saved to baseline audit cost
Experiment Running evaluation
Quantifies operational cost savings from intelligent audit allocation
Attack Rate Reduction
Percentage decrease in successful attack events vs baseline
Experiment Running evaluation
Measures security improvement from framework deployment
Accuracy = (TP+TN)/(TP+TN+FP+FN)
Overall correctness across all classes
Experiment Running evaluation
Standard classification accuracy for anomaly detection
Recall = TP/(TP+FN)
Proportion of actual anomalies correctly identified
Experiment Running evaluation
Measures sensitivity to true anomaly events
F1 Score = 2×(Precision×Recall)/(Precision+Recall)
Harmonic mean balancing precision and recall
Experiment Running evaluation
Balances false positives and false negatives under class imbalance
SCADA Calculated Channel
value = f(input_channels, time, drift_factor)
Rapid SCADA Live
Generates simulated telemetry with trend and drift for live testing
Feature Contribution
Proportional deviation weight for explainability
Rapid SCADA Live
Identifies which features drove each anomaly score for operators

## Slide 19
Mathematical Formulations and Methodology (Part 2: Evaluation Metrics)
Formula Type
Simple Meaning
Used In
Purpose
Risk Mitigation
Percentage of high-risk events prevented or mitigated
Experiment Running evaluation
Measures effectiveness in reducing operational risk exposure
Cost Efficiency
Ratio of audit resources saved to baseline audit cost
Experiment Running evaluation
Quantifies operational cost savings from intelligent audit allocation
Attack Rate Reduction
Percentage decrease in successful attack events vs baseline
Experiment Running evaluation
Measures security improvement from framework deployment
Accuracy = (TP+TN)/(TP+TN+FP+FN)
Overall correctness across all classes
Experiment Running evaluation
Standard classification accuracy for anomaly detection
Recall = TP/(TP+FN)
Proportion of actual anomalies correctly identified
Experiment Running evaluation
Measures sensitivity to true anomaly events
F1 Score = 2×(Precision×Recall)/(Precision+Recall)
Harmonic mean balancing precision and recall
Experiment Running evaluation
Balances false positives and false negatives under class imbalance

## Slide 20
Audit Decision Logic: Risk-Aware Resource Allocation
1
Step 1: Risk Scoring
2
Step 2: Threshold Evaluation
3
Step 3: Primary Live Actions
4
Step 4: Prioritization Under Constraints
5
Step 5: Operational Conversion
Compute a composite risk score from anomaly magnitude combined with asset criticality to quantify potential impact and urgency.
Evaluate the computed risk against predefined thresholds to determine whether audit escalation is required for further action.
Decide on immediate operational actions, selecting either MAINTAIN AUDIT for baseline monitoring or INCREASE AUDIT for intensified scrutiny.
Prioritize auditing of high-risk assets when resources are constrained, ensuring the most critical risks receive attention first.
Translate anomaly detection outputs into actionable operational directives that are clear, interpretable, and executable by teams.

## Slide 21
Explainability: Feature-Level Transparency for Operator Trust
Top contributing features
Feature importance ranking
Deviation-based logic
Operator dashboard view
Maintains transparency
Top contributing features are identified for each anomaly score, enabling operators to see which inputs drove the detection.
Feature importance ranking supports operator interpretation by ordering signals by their contribution to the anomaly.
Deviation-based logic preserves traceability and reasoning clarity, linking anomalies to measurable shifts in feature behavior.
Operator dashboard displays anomaly score, audit decision, and a concise explanation summarizing top contributing features for a selected agent.
Maintains transparency rather than black-box alerting, ensuring operators can trust and verify automated flags.

## Slide 22
Implementation Stack: Modular Deployment-Oriented Platform
1
Backend
2
Frontend
3
SCADA
4
Bridge
5
Execution environment
FastAPI for SCADA ingest, anomaly scoring, audit logic, and explanation generation
Next.js dashboard with separated Experiment and Live workspaces
Rapid SCADA Webstation with a 300-channel calculated model
PowerShell-based authenticated API retrieval with batched ingestion
Standard workstation prioritizing API responsiveness

## Slide 23
Testing and Validation: Structured Implementation Test Cases
1
TC-01
2
TC-02
3
TC-03
4
TC-04
5
TC-05 to TC-08
Baseline behavior validation under normal operating profile
Anomaly scoring validation with injected deviations
Audit escalation logic when risk score exceeds threshold
Rapid SCADA integration via Web API and authenticated bridge
Batched ingest, dashboard correctness, explainability, runtime stability - All test cases passed

## Slide 24
Live SCADA Validation: 100-Agent Operational Confirmation
Verification
Pipeline Validation
Telemetry Retrieval
Integration
Operational Note
100 live agents, 0 non-live agents confirmed operational
Full SCADA-to-backend-to-dashboard pipeline validated
Continuous real-time telemetry retrieval through Web API
Successful integration with anomaly scoring and audit decision layers
SCADA pipeline operational; telemetry generated via calculated channels (not physical devices)

## Slide 25
Primary Thesis Result (N=100): Validated Operational Profile
Attack Rate Reduction
Cost Efficiency
Risk Mitigation
Accuracy
Recall
F1 Score
Audit Coverage
77.47%
Measured reduction in successful attacks compared to baseline
54.83%
Operational cost savings relative to prior implementation
95.93%
Effectiveness in mitigating identified operational risks
99.14%
Overall accuracy of the operational model
100.0%
Sensitivity of detection mechanisms
25.67%
Harmonic mean of precision and recall
100.0%
Proportion of operations covered by audit procedures
Note: Exceeds base paper on all primary operational metrics

## Slide 26
Base Paper vs Proposed System Comparison
Validated N=100 configuration demonstrates substantial improvements across all primary operational metrics, confirming the effectiveness of SCADA-integrated explainable audit framework.
Metric
Base Paper
Proposed System (N=100)
Improvement
Cost Efficiency
42.5%
54.83%
+12.33%
Audit Coverage
93.8%
100%
+6.2%
Accuracy
98.4%
99.14%
+0.74%
Risk Mitigation
87.9%
95.93%
+8.03%

## Slide 27
Scaled Results: Performance Across Grid Sizes
System evaluated across N=100, N=200, and N=500 agents to analyze scalability characteristics, revealing tradeoffs between mitigation strength and operational efficiency.
Grid Size
Attack Reduction
Cost Efficiency
Risk Mitigation
Accuracy
Latency (avg)
N=100
77.47%
54.83%
95.93%
99.14%
58.79 ms
N=200
75.13%
49.22%
96.65%
99.01%
118.85 ms
N=500
34.20%
73.19%
82.36%
99.08%
288.46 ms

## Slide 28
Discussion: Tradeoffs Between Efficiency, Mitigation, and Scale
Observation 1
Observation 2
Observation 3
Observation 4
Observation 5
Medium-scale (N=200) preserves strongest mitigation performance at 96.65%, indicating an optimal balance between scale and detection effectiveness.
Large-scale (N=500) achieves higher cost savings of 73.19% but experiences weaker mitigation performance at 82.36%, reflecting a tradeoff with scale.
Attack reduction declines significantly at N=500 to 34.20%, suggesting diminishing returns for mitigation as scale increases.
System latency scales linearly across tested sizes, and the system remains operationally usable across the evaluated range.
There is an inherent tradeoff between operational efficiency and detection effectiveness in distributed environments that must be managed when choosing scale.

## Slide 29
Limitations: Scope and Deployment Constraints
1
2
3
4
5
Telemetry generated via Rapid SCADA calculated channels, not physical field devices
System represents operational prototype, not full real-world utility deployment
Baseline values currently hand-engineered rather than adaptively learned
F1 Score reflects class imbalance; minority anomaly detection sensitivity lower
Scalability beyond N=500 not yet evaluated; live workspace tested at N=100 only

## Slide 30
Conclusion: Bridging Research and Operational Implementation
Integrated Systems
Workspace Separation
Empirical Validation
Explainable Framework
Operational Prototype
Successfully integrated anomaly detection, audit intelligence, and SCADA monitoring into a unified pipeline for end-to-end operational observability and response.
Clear workspace separation was enforced to guarantee experimental isolation and operational correctness, minimizing cross-environment interference.
Validated an N=100 configuration which surpasses the baseline paper on primary operational metrics, demonstrating measurable performance improvements.
Demonstrates a practical explainable cyber-physical audit framework that supports interpretable alerts and root-cause insights for operators.
Delivered a strong operational prototype that maintains transparency about deployment scope, limitations, and intended operational contexts.

## Slide 31
Future Work: Pathway to Real-World Deployment
1
Step 1: Device Integration
2
Step 2: Adaptive Baselines
3
Step 3: Scalability Testing
4
Step 4: Multi-objective Optimization
Integration with physical field devices for true operational telemetry
Adaptive baseline learning replacing hand-engineered reference values
Extended scalability testing beyond N=500 agents
Multi-objective optimization balancing mitigation, cost, and latency

## Slide 32
Thank You
Questions and Discussion - SmartGrid AI Audit Framework | Aditya Sanjay Jadhav (242050010) | Guide: Shrinivas Khedkar | VJTI Mumbai